## Slide 1: Design, Fabrication, and Testing of Lander Ramps For Rover Egress
Zack Morrison
Hahna Alexander
Anton Galkin
11/21/2011
Notes: Anton

## Slide 2: Fabrication is Underway
Parts arrived & inventoried
Machining started
Waterjet cutting underway

## Slide 3: Outline
Problem statement
Motivation
Results
Contribution
Future work

## Slide 4: Problem Identification and Motivation
Rover egress: the method by which the rover descends from the top of the Lander to ground.
  Mission success depends on successful egress.
Implement mechanism to enable rover egress
Problem considerations:
  Primary: rover safety, deployment reliability
  Secondary: mass, cost

## Slide 5: Approach
Researched design parameters and constraints
Compared designs in Pugh Chart
Selected 2 segment design
Extensive CAD modeling
Analysis: ANSYS, SolidWorks, Matlab
Created manufacturing drawings
Developed bill of materials, ordered parts
Fabrication

## Slide 6: Parts Arrived & Inventoried

## Slide 7: Machining Started

## Slide 8: Metal & Drawings Sent to NREC

## Slide 9: Ramp Deployment Torque
Springs provide proper deployment torque
SolidWorks Motion Analysis & hand calculations
Chart: Angle (Degrees)
| 0.15 | 2.2799999999999998 | 4.03 | 6.12 | 9.4499999999999993 | 12.01 | 14.68 | 17.75 | 20.28 | 22.68 | 25.38 | 27.47 | 29.51 | 31.83 | 35.82 | 38.49 | 42.1 | 46.19 | 48.94 | 53.02 | 55.59 | 56.62 | 58.29 | 59.61 | 61.4 | 63.04 | 64.62
Torque from 6 Springs | 375.9959 | 377.628 | 378.4072 | 378.6486 | 377.7447 | 375.9672 | 372.9882 | 368.4109 | 363.4169 | 357.9434 | 350.7291 | 344.4127 | 337.6761 | 329.2691 | 313.0751 | 301.0965 | 283.4585 | 261.538 | 245.7354 | 220.799 | 204.3806 | 197.5962 | 186.4653 | 177.5347 | 164.9357 | 159.0877 | 142.6498
Torque Required from Simulation | 328.4159 | 359.5395 | 358.9244 | 358.2222 | 357.4266 | 356.5249 | 355.5023 | 354.3423 | 353.0271 | 351.5388 | 349.859 | 347.9701 | 345.855 | 343.4976 | 340.8831 | 337.9977 | 334.829 | 331.366 | 327.5986 | 323.5182 | 319.1172 | 314.3888 | 309.3277 | 303.929 | 298.1891 | 292.1051 | 285.675 | 278.8977 | 271.773 | 264.3013 | 256.484 | 248.3229 | 239.8207 | 230.9804 | 221.8054 | 212.2991 | 202.4648 | 192.3051 | 181.8221 | 171.0164 | 159.887 | 148.4312 | 136.6442 | 124.5191 | 112.048 | 99.2225 | 86.0352 | 72.4829 | 58.5683 | 44.3034 | 29.7117 | 14.829

## Slide 10: Contribution
Extendibility of ramp design for future iterations
Deployment kinematics
Feasibility of ramp design
Visual impact

## Slide 11: Semester Schedule

## Slide 12: Future Work
ANSYS analysis of composite feasibility
ANSYS vibration testing
Implementation of extensive test plan
  Small model rover egress
  Geometry
  Deployment reliability
Optimization of joint and body parameters
  Weight
  Stiffness
Class requirements: paper, final presentation, 1 blog

## Slide 13: Questions?

## Slide 14: Metrics
Analysis and selection of best design
Detailed CAD drawings and manufacturing plan
Ramp fabrication
Ramp deployment test
Rover egress test using a mockup rover
Simulations for future implementation